EE473/538 CAD Lab1
Due Tuesday, Jan. 25th, 2022

The NMOS transistor drain current in saturation is modeled as I_D &=& \frac{k'}{2}\frac{W}{L}(V_{GS}-V_{t})^2(1+\lambda V_{DS}) .

The drain current in triode region is modeled as I_D &=& k'\frac{W}{L}\left[(V_{GS}-V_{t} - \frac{V_{DS}}{2})V_{DS} \right](1+\lambda V_{DS}) .

Device parameters are k' = 194 \mu A/V^2 , W = 10 \mu m , L = 1 \mu m , and \lambda = 0.024V^{-1} .

Given V_{SB}=0 , the threshold voltage is simplified to V_t = V_{t0} = 0.6V . The drain current is rewritten with the above parameters such that I_D = 0.97\cdot10^{-3}(V_{GS}-0.6)^{2}(1+0.024 V_{DS}) . This can be further simplified to I_D \approx (V_{GS}-0.6)^{2} mA for this V_{GS} sweep.

At V_{GS}=0 , the device is turned off.

At V_{GS} = 1.5, 3V the device first enters the triode region, then moves to saturation when V_{GS}-V_t \leq V_{DS} .

Figure 1: NMOS Drain Current: VGS=[0.5, 1.5, 3]V

The body voltage is no longer neglected. The threshold voltage is modeled as
V_t &=& V_{t0} + \gamma(\sqrt{2\phi_f + V_{SB}}-\sqrt{2\phi_f}) \geq 0.6V .

The drain currents will be less than the previous plots for the same values of V_{GS} .

Figure 2: NMOS Drain Current: VSB=[0, 0.5, 1]V