EE 473/538 Linear IC Design
HW2 February 11, 2022
Kevin Egedy

Figure: Sedra Smith Microelectronic Circuits

Define V_y at the point between R_a and R_b .

Initially, all channels are closed because V_{DS} = V_{GS} < V_{th} and no current runs through R_a and R_b .

V_{DS} increases such that V_x = V_y = V_{GS} = V_{th} .

The channel is no longer pinched and allows current.
Both M_5 and M_6 turn on and the drain current through M_5 turns on the remaining circuit.

Now the channel is induced and V_{DS} keeps increasing, allowing more drain current through M_6 .

The voltages at V_y and V_x are defined as

V_y = V_{DD} – I_{D6} R_a and V_x = V_{DD} – I_{D6} \left(R_a + R_b\right) = V_y – I_{D6} R_b .

As I_{D6} continues to grow, V_y decreases and also V_x decreases.

It is guaranteed that V_x < V_{th} when

V_{DD} – I_{D6} \left(R_a + R_b\right) < V_{th} where

I_{D6} = \mu_n C_{ox} \left(\dfrac{W}{L} \right)\left(V_{gs} - V_{th} \right)^2 \ \bigg|_{V_{gs} = V_{DD}-I_{D6}R_a}